## Slide 1: A Status Report on SMB Direct for Samba
Richard Sharpe
Samba Team & Panzura

## Slide 2: Agenda
How we got here
The relevant protocol details
Overview of the structure of Samba
The options
The Linux driver option
Samba changes needed
Status
Acknowledgements
Further Information

## Slide 3: How we got here
2011 Microsoft Introduced SMB2.2 and SMB Direct at SDC 2011
2011 I played around with RDMA
May 2012 Microsoft gave SMB2.2/3.0 tutorial at Samba XP
Some of us thought about it
Mellanox supplied some IB cards to some Samba team members
May 2013 Microsoft gave further presentations about SMB3.0
After that I started to get serious about it

## Slide 4: How we got here, cont
June 2013 I had a conference call with Mellanox to discuss options
August 2013 I started circulating a design document

## Slide 5: The relevant protocol details
Client connects via TCP first (port 445)
  SESSION_SETUP obtains Session ID
  Connects to a share
Queries the network interfaces
  FSCTL_QUERY_NETWORK_INTERFACE_INFO
Place an RDMA Connection to server on port 5445
Brings up SMB Direct Protocol Engine
Transport SMB PDUs

## Slide 6: Relevant Protocol Details, cont
Client sends SMB2/3 Negotiate request
  Dialect 0x300 (SMB 3)
  SMB2_GLOBAL_CAP_MULTI_CHANNEL in Capabilities field
Server responds
Client sends SMB2/3 SESSION_SETUP request
  SMB2_SESSION_FLAG_BINDING in flags
  Session ID same as the one obtained for first connection/session

## Slide 7: Relevant Protocol Details, cont
SMB Direct
  Thin layer on RDMA
  Transports SMB3 PDUs
  Negotiate request and response
  Data transfer message
  Buffer descriptor structure

## Slide 8: Relevant Protocol Details, cont
SMB2 spec section 4.8 gives an example
Client
Server
Negotiate
Session Setup
Tree Connect
FSCTL_QUERY_NETWORK_INTERFACE_INFO
Negotiate
Session Setup
TCP
TCP/RDMA
Then on a separate connection

## Slide 9: SMB Direct
Small protocol
  Transports SMB PDUs over RDMA
  Support for RDMA READ and RDMA WRITE
Negotiate exchange
  Sets parameters
PDU transfer phase

## Slide 10: Overview of the structure of Samba
Master smbd
  Fork model
  Accepts all incoming TCP connections
  Forks a new process for each TCP connection
  Does not handle any SMB PDUs
Separate process per connection
Uses poll/epoll and an event mechanism for handling SMB PDUs and other events
Separate SMB and SMB2/3 code paths

## Slide 11: Samba Structure
Client
Server
primary
smbd
child
smbd
First Connection
Connection
handed off
?
Second Connection
RDMA port 5445
Port 445

## Slide 12: Issues
How to get RDMA connections/sessions associated with the original TCP connection/session?
  Clients always connect to port 5445 for RDMA
  Mellanox folks tell me you cannot transfer RDMA connections from one process to another
    Too much state, especially memory state

## Slide 13: The Options
Convert Samba to a threaded model
  Everything in one address space
Separate process to handle all RDMA connections and data transport
Kernel driver to handle RDMA

## Slide 14: Convert Samba to threaded model
Would simplify multi-connect with TCP and RDMA
A lot of work
  The code still has many assumptions around each TCP connection handled in a separate process
Problems?
  Max open FDs?
  Posix Threads and UIDs and GIDs

## Slide 15: Separate RDMA handler process
master
smbd
child
smbd
RDMA handler
Initial TCP Connection
RDMA Connection(s)
Shared memory
1. Negotiate
2. Session Setup
3. Tree Conect
4. FSCTL…
1. Negotiate
2. Session Setup
child
smbd

## Slide 16: Issues?
Layering violation!
  We are going to have to engage in a layering violation anyway unless we have everything in the kernel or everything in one process
A context switch per RDMA SEND, RECV, READ, WRITE
  Big performance hit

## Slide 17: Kernel driver to handle RDMA
smbd 1
smbd n
shared memory
smbdirect driver
RDMA support (rdmacm etc)
IB Device Driver(s)
smbd 0

## Slide 18: Kernel driver, cont
smbd
smbdirect
driver
RDMA
support
Negotiate
Session Setup
Tree Connect
FSCTL_QUERY_NETWORK_INTERFACE_INFO
1
2
Negotiate
Session Setup
3
4
First connection
Register session ID
RDMA connection
PDUs

## Slide 19: Issues
Layering Violation
Will require kernel knowledge as well as Samba knowledge

## Slide 20: The Linux driver option
Character mode device
SMB Direct implementation
First part of SMB 3.0
  Up to Session Setup because that is when we know which smbd to dispatch to
Uses the in-Kernel RDMA support
  Rdmacm etc

## Slide 21: Kernel driver, cont
ioctls
  Setup SMB Direct parameters
  Retrieve memory params
  Send and retrieve PDUs
    RDMA SEND and RDMA RECV
  Initiate RDMA READ and RDMA WRITE
  No BKL for ioctl_unlocked
mmap
  For RDMA READ and RDMA WRITE memory

## Slide 22: Kernel driver, cont
IOCTLs
SMB Direct engine
RDMA Support
  Event/callback driven
  Memory Registration
RDMA READ/WRITE Support

## Slide 23: IOCTLS
SET_SMBD_PARAMETERS
SET_SMBD_SESSION_ID
GET_MEM_PARAMS
GET_SMBD_EVENT
  Includes received PDUs, send complete, etc
SEND_PDU
RDMA_READ_WRITE
SET_SMBD_DISCONNECT

## Slide 24: IOCTLS, cont
Amortize mode switch
  Get, send, etc, multiple buffers per IOCTL
Buffer
Count of objects
Obj 1
Obj 2
…
Obj n
Obj 1
Obj 1
Type
Len
Object
Extra

## Slide 25: Samba changes needed
Option to specify SMB Direct supported
Open smbdirect device and configure params
Register session ID with smbdirect driver
Allow input of SMB 3.0 PDUs from smbdirect
Modify READ and WRITE code paths
  Issue RDMA READ and RDMA WRITE via smbdirect
  When Buffer Descriptors present

## Slide 26: Goals
Get something working
  Allow others to contribute
Improve performance
  With help of others

## Slide 27: Status
A start has been made
Driver loads and unloads
  Listens for RDMA connections
  Working through the details of registering memory
Understand the Samba changes needed
Weekend project!
https://github.com/RichardSharpe/smbdirect-driver

## Slide 28: Acknowledgements
In no particular order
Microsoft for documenting SMB Direct and SMB2/3
Mellanox for IB cards and support
Tom Talpey for feedback and encouragement
Or Gerlitz for suggestions around the correct kernel interfaces to use
Samba team members for feedback and encouragement

## Slide 29: Further information
SMB2: http://msdn.microsoft.com/en-us/library/cc246482.aspx
SMB Direct: http://msdn.microsoft.com/en-us/library/hh536346.aspx
Samba: www.samba.org